## Slide 1
CEB 4053
Transport
Phenomena
Chapter 1 · Introduction
Momentum
Heat
Mass
Department of Chemical Engineering · Universiti Teknologi PETRONAS
Notes: Open by asking: what do a tennis ball, a cooking pot, and a distillation column have in common? Park the question — it gets answered in slide 4.

## Slide 2
THE PREMISE
Three subjects you already know — taught as one
You have studied fluid mechanics, heat transfer, and mass transfer as separate courses. This chapter argues they are three readings of a single physical idea, and that recognising it saves you from solving the same problem three times.
1
Explain the importance and the general concept of Transport Phenomena.
2
Explain the similarity between momentum, energy, and mass transport processes.
3
Derive general transport equations for momentum, energy, and mass transport.
Learning outcomes for this chapter
2
Notes: Outcome 2 is the one that matters. If they leave understanding only that, the chapter has done its job.

## Slide 3
ACCREDITATION
How this maps to your programme
CLO 1
Explain the theoretical aspect of momentum, mass and energy transport.
Assessed through: derivations, problem sets, and the final examination.
PO 1
Apply knowledge of mathematics, science and engineering fundamentals to the solution of complex chemical engineering problems.
Programme outcome, Washington Accord alignment.
3

## Slide 4
The whole chapter in one line
Flux = − (diffusivity) × (gradient)
Momentum, heat, and mass all obey this. Only the names change.
MOMENTUM
τyx = − ν · d(ρvx)/dy
Newton's law of viscosity
HEAT
qy = − α · d(ρĈpT)/dy
Fourier's law
MASS
JAy = − DAB · dcA/dy
Fick's law
Try it live → the transport analogy widget
4
Notes: Open the widget here. Flatten the gradient slider — all three fluxes go to zero together. That single demonstration is the chapter thesis.

## Slide 5
DEFINITIONS
What is actually being transported
M
Momentum transfer
Momentum moves through a fluid from one location to another
The subject you know as fluid mechanics
Driven by a velocity difference
H
Heat transfer
Thermal energy moves from one location or stream to another
Conduction, convection, radiation
Driven by a temperature difference
D
Mass transfer
Net movement of a species from one stream or phase to another
Absorption, distillation, drying, adsorption
Driven by a concentration difference
In every case: something moves because a difference exists, and the movement acts to remove that difference.
5

## Slide 6
INDUSTRIAL CONTEXT
All three, in every unit you will ever design
Exothermic CSTR
Flow in and out, mixing, coolant circulation · reaction heat crossing the jacket wall · reagents meeting to react
Shell-and-tube exchanger
Hot and cold streams driven through shell and tubes · heat crossing the tube wall between them
Distillation column
Feed in, liquid down, vapour up · condenser and reboiler duty · light and heavy components redistributing between phases
Ammonia synthesis reactor
Gas through a packed bed · strongly exothermic duty removal · N₂ and H₂ diffusing to catalyst sites
Dots show which transport modes are active.
6
Notes: Ask the class to name a unit operation where only one mode is active. It is a harder question than it sounds — that is the point.

## Slide 7
SCALE
Three levels of description
1
Macroscopic
What crosses the boundary of the whole vessel?
Overall balances on mass, momentum, and energy. No interest in what happens inside.
Macroscopic balance equations
2
Microscopic
What happens in a small region inside the vessel?
Profiles of velocity, temperature, and concentration as functions of position and time.
Equations of change
3
Molecular
What are the molecules themselves doing?
Where the transport coefficients μ, k, and DAB come from in the first place.
Kinetic theory
Bird, Stewart & Lightfoot, Transport Phenomena, 2e — Fig. 0.2-1
7

## Slide 8
SCALE, CONCRETELY
The same gas, described two ways
MACROSCOPIC
Pressure. Temperature.
One number for the whole vessel. What a gauge reads. Sufficient for an energy balance, useless for a boundary layer.
MICROSCOPIC
Velocity. Momentum.
The kinetic motion of individual molecules. Average them and pressure and temperature emerge — they were never separate quantities.
Temperature is not a property a molecule has. It is a statement about a population of them.
8

## Slide 9
The shape of every transport problem
Rate =
driving force
resistance
Learn to read any transport problem this way and the algebra follows. Identify what is driving the transfer, identify what is impeding it, and the constitutive law writes itself.
Momentum
Newton's law
Heat
Fourier's law
Mass
Fick's law
9

## Slide 10
MOMENTUM TRANSPORT
Newton's law of viscosity
τyx = − μ · dvx/dy
(1.1-2)
Read it as a force
τyx is the force in the x-direction acting on a unit area whose normal points in the y-direction. Momentum is being handed sideways, from fast fluid to slow.
The experiment behind it
Fluid at rest between two plates, separation Y.
The lower plate is set in motion at velocity V.
Momentum diffuses upward; a velocity profile builds.
At steady state the profile is linear: F/A = μV/Y.
Kinematic viscosity
ν = μ / ρ
Units: m²/s. Remember this — it is what makes the analogy work three slides from now.
10
Notes: Emphasise the minus sign: transport runs down the gradient. That is the second law appearing inside a constitutive equation.

## Slide 11
ENERGY TRANSPORT
Fourier's law of heat conduction
qy = − k · dT/dy
(9.1-2)
The identical experiment
A solid slab initially at T₀. The lower face is raised to T₁. Heat diffuses upward, a temperature profile builds, and at steady state Q/A = k(T₁−T₀)/Y.
Compare with the previous slide
Flux
τyx
qy
Coefficient
μ
k
Gradient of
velocity
temperature
Diffusivity
ν = μ/ρ
α = k/ρĈp
Thermal diffusivity
α = k / ρĈp
Units: m²/s again. Same units as ν, and that is not a coincidence.
11

## Slide 12
MASS TRANSPORT
Fick's law of molecular diffusion
jAy = − ρDAB · dωA/dy
(17.1-4)
The identical experiment, a third time
A slab of fused silica, thickness Y, with helium held at mass fraction ωA0 on one face. Helium diffuses through; a concentration profile builds; at steady state the flux is constant.
Notation
jAy
molecular mass flux of species A
ρ
density of the two-component system
DAB
mass diffusivity of A through B
ωA0
solubility, as a mass fraction
Mass diffusivity
DAB
Units: m²/s. Three different physical processes, three coefficients, one set of units.
12

## Slide 13
Why the shared units matter
Three diffusivities. One dimension.
ν, α, and DAB all carry units of m²/s. Their ratios are therefore dimensionless — and each one tells you which front travels further in a given time.
Pr
Prandtl
ν / α
momentum vs heat
Sc
Schmidt
ν / DAB
momentum vs mass
Le
Lewis
α / DAB
heat vs mass
Watch the three fronts race → the diffusivity visualiser
Solve one boundary-layer problem properly and you have solved all three.
13
Notes: Run the visualiser with engine oil selected — momentum runs away while mass barely moves. Then switch to mercury, where heat outruns momentum and Pr drops below one.

## Slide 14
CHECK YOUR UNDERSTANDING · RECALL
Q1
A copper bar has one end held hot and the other cold. Which law describes the heat flowing along it?
A
Newton's law of viscosity
B
Fourier's law of heat conduction
C
Fick's law of molecular diffusion
D
None — no transport occurs in a solid
Show of hands before you move on.
14
Notes: Answer: B. Reinforce that the minus sign means heat runs from hot to cold, never the reverse. Option D is worth addressing directly — conduction in solids is the cleanest case of diffusive transport there is, precisely because no bulk motion complicates it.

## Slide 15
CHECK YOUR UNDERSTANDING · APPLY
Q2
A fluid has Pr = 0.02. In a boundary layer along a heated plate, which layer is thicker?
A
The velocity boundary layer
B
The thermal boundary layer
C
They are the same thickness
D
It cannot be determined from Pr alone
Pr = ν / α. Penetration depth scales as the square root of the diffusivity.
15
Notes: Answer: B. Pr well below 1 means alpha is much larger than nu, so heat penetrates further than momentum — the thermal layer is thicker. Liquid metals sit here; mercury has Pr around 0.025. Worth running the diffusivity visualiser on the mercury setting at this point. A common wrong path is students reading Pr < 1 as "less heat transfer" rather than "heat diffuses faster relative to momentum".

## Slide 16
CHECK YOUR UNDERSTANDING · ANALYSE
Q3
Two gases share the same ν but differ in DAB by a factor of four. After the same elapsed time, how do their concentration fronts compare?
A
The faster front has travelled 4 times further
B
The faster front has travelled 2 times further
C
The faster front has travelled 16 times further
D
Both fronts have travelled the same distance
Penetration depth ~ √(D·t). Their Schmidt numbers differ by a factor of four.
16
Notes: Answer: B. The square-root dependence is the point: quadrupling the diffusivity only doubles the penetration depth. Students who answer A have applied a linear relationship and this is the moment to correct it, because the same square-root scaling governs every unsteady penetration problem they will meet for the rest of the course. Follow up by asking how much longer the slower gas needs to reach the same depth — the answer is four times as long, and that asymmetry surprises them.

## Slide 17
CHAPTER 1 CLOSE
What you should be able to do now
State the general form
Flux is proportional to a gradient, scaled by a diffusivity, and directed down the gradient.
Name the three laws
Newton's, Fourier's, and Fick's — and say what each one transports.
Identify the mode
Given any unit operation, say which transport processes are active and why.
Use the analogy
Recognise Pr, Sc, and Le as statements about which front travels further.
All course tools: github.com/bawadi73/transport-phenomena
17

## Slide 18
BEFORE THE NEXT LECTURE
Take-home exercise
Both tools run in any browser, on a phone or a laptop. Nothing to install. Bring your written answers to the next session.
A
The transport analogy widget
Set the gradient to zero. Record what happens to all three fluxes, and explain why in one sentence.
Now raise the diffusivity to maximum with the gradient still at zero. Does anything change? Why not?
Write the general form of the flux law from memory, without looking at your notes.
B
The diffusivity race
Run all four fluids. Tabulate Pr, Sc, and Le for each one.
Identify which fluid has Pr below 1, and explain physically why that is so.
Engine oil: after 60 s, how many times further has momentum penetrated than mass? Verify against the square-root scaling.
Both tools: github.com/bawadi73/transport-phenomena
18
Notes: Task A is a five-minute check that the core idea landed. Task B takes longer and rewards care — the oil case gives a ratio near 1500, which surprises them enough to make the square-root scaling memorable. Collect the tables at the start of the next session.